## Slide 1
Notes: 參賽項目名稱： 根深柢固
<number>

## Slide 2
Background
.
Over the past few years, some incidents, falling down of pedestrian near trench decking area, happened due to the movement of un-secure pedestrian decking. These incidents directly or indirectly caused injuries to the pedestrians.
CLPE carrying cable trench work at busy urban area of Kowloon, included Tsim Sha Tsui, Yau Ma Tei & Mong Kok.
To minimize the inconvenience caused to the general public, pedestrian decking is commonly used in the market to cover the trench for temporary reopen the area.
Commonly use decking but frequently find movement
During site inspection found the movement of decking
Notes: 中電工程响最繁忙的九龍心臟地帶負責地下電纜鋪設工程，當中包括尖沙咀，油麻地及旺角等地方。
為了盡量減少對公眾造成不便，纖維蓋板被廣泛應用在行人路挖掘工程中，臨時將道路重新開放比公眾。
但係，在過去的幾年中，不時因為纖維蓋板走位而發生行人跌落壕坑既事故。
<number>

## Slide 3
A real incident case (Non-CLP)
A woman fall down in a work site due to un-secure pedestrian decking.
Background
Un-secured decking may caused
Personal injury
Damage to underground utility
Fire, explosion
Third party claim or public complaint
Highways Department’s non-compliance report
Extra workforce from handling incidents, complaints, and media.
Negative image on Company
Un-secured decking may caused serious consequence
Notes: 唔穩固既纖維蓋板可能造成以下問題：
人身傷害
損毀地下設施
火警或爆炸
第三者索賠或市民投訴
路政署的違規報告
額外的人手處理事故，投訴和媒體的查詢
對公司的負面形象。
<number>

## Slide 4
Fish-bone Analysis
To develop a possible solution to prevent the movement of trench decking
Notes: 根據魚骨圖分析法，將纖維蓋板走位的成因分為人，機，物，法，環五類。當中發現纖維蓋走位的主因係纖維蓋板鋪設的手工，工地環境引致鋪設困難，及纖維蓋板被特殊外力影響，例如手推車。
了解咗纖維蓋板走位成因後，下一步係用咩方法可以有效防止走位。
<number>

## Slide 5
Possible Solutions
Can we design a tool to provide a mechanical means?
Notes: 我們曾考慮不同的解決方法，包括
加大纖維蓋板同地面磨擦，例如以麻包攝底。但只可以減少走位機會，未可以完全避免纖維蓋板走位。
將纖維蓋板互相連接，加大重量。但如果挖掘位置細小，只有一兩件纖維蓋板，這方法並唔可行。
用英泥沙圍邊固定纖維蓋板，英泥沙一段時間會出現裂痕，要花費工人時間檢查同保護。
用石屎釘打落地面，特出既釘有機會危及途人，另外磚面路唔可行。
<number>

## Slide 6
Design
A mechanical propping mounted under the decking
That mechanical propping can mounting into the honeycomb under the decking and fix on the trench.
Notes: 因應各方考慮，我地設計咗一個機械支撐架：叫根深柢固。佢係由壕坑工地閘板既橫頂，加上兩個活動式定位器改裝而成。根深柢固安裝簡易，只要將橫頂調較至合適長度放於壕坑上，再將纖維蓋板放上，確保根深柢固定位器墈入膠板底部的蜂窩凹位內就完成。
<number>

## Slide 7
Implementation
Trial use on Sept 2012, and fully implement on Jan 2013
After the trial use in several project sites, the design was reviewed by management to go through an evaluation to ensure that the charge will not cause any side impact. The result of the review is satisfaction.
Apply on concrete pavement
Apply on pavement block
Notes: 於上年9月開始，我地選擇咗幾個工地試用根深柢固，發現就算响繁忙路段，採用根深柢固既纖維蓋板完全無出現走位。經過前線同事回應，根深柢固再三研究及改良，根深柢固可用响石屎路面及磚面地。經過評估，結果十分滿意，並於２０１３年大量採用。
<number>

## Slide 8
Got 3E & 2S as the result:
  3E
  Effective, provide a secure and safe decking;
  Efficient, easy to install, remove and reinstate;
  Environmental Friendly, avoid waste and even Green for the environment.
  2S
  Simple, no special skill required;
  Saving, low investment and even with cost saving.
Result
Effective, Efficient, Environmental Friendly, Simple, & Saving
Notes: 就根深柢固得出3E2S結果：
3E包括
Effective, 實際，根深柢固為纖維蓋板提供一個安全可靠的固定裝置;
Efficient , 效率，根深柢固易於安裝，拆除和再次安裝;
Environmental, 環保，避免資源浪費及對保護環境作出一份力。
2S包括
Simple, 簡單，無需技能要求;
Saving, 節省，低投資高回報，減省人力資源處理纖維蓋板走位問題。
<number>

## Slide 9
Benefits
Tangible Benefits
Time & cost saving from daily decking rectification
Time & cost saving from extra workload on reply & handling of incident case, HyD’s NC, and complaint
Saving from the loss of incident
Saving in insurance cost with improved incident rate
Intangible Benefits
Enhance the image of the Company to frontline workmen and relevant government departments
Reduce the numbers of Highways Department’s NC due to improper trench decking
Reduce the numbers of complaint from public due to movement of trench decking
Reduce the numbers of incident of injury reimbursement cost arise from public due to improper trench decking
Reduce the numbers of legal action from public.
Public safety is one of our major concerns
Notes: 實際好處
節省時間和費用，處理纖維蓋板走位問題
節省額外的工作量去處理路政署的NC和投訴
節約保險成本與改進的事故率
無形效益
提高公司形象
減少路政署的ＮＣ
減少因纖維蓋板走引致的公眾意外
減少因公眾意外所引發的法律行動。
最後保障公眾安全是根深柢固一個最大好處。
<number>

## Slide 10
End
Notes: <number>

## Slide 11
3 difference versions for the design
First Design:
A projecting plate mounting into the honeycomb
Second Design:
Two projecting plates mounting into the honeycomb
Final Design:
A projecting channel mounting into the honeycomb:
Supplement Information (Standard Drawing)

## Slide 12
於探孔位置，繁忙街道，巴士站或泊車位附近等位置，可以根深柢固防止行人板走位。
Supplement Information (Installation Gridline)
Notes: <number>

## Slide 13
  步驟一：
  調較合適長度安放於壕坑上
  留意馬騮頭曲呎碼需緊貼路面及平放
  方通固定碼需向上方調較
Supplement Information (Installation Gridline)

## Slide 14
  步驟ニ：
  按放1200mm膠冚板
  調較固定通位確保方通墈入膠板底部凹位
  用手工具收緊頂通固定螺絲帽
  再調較固定方通並收緊固定螺絲帽
Supplement Information (Installation Gridline)

## Slide 15
  步驟三：
  用手測試冚板穩固程度
  向斜邊方向推
  向止口方向推
Supplement Information (Installation Gridline)

## Slide 16
  步驟四：
  重覆步驟一至三於合適固定位置
Supplement Information (Installation Gridline)

## Slide 17
  步驟五：
  於冚板上步行並留意固定位置異常
  有否凸起
  有否磨擦聲發出
  冚板斜邊緊貼路面
Supplement Information (Installation Gridline)

## Slide 18
  磚地加木框鞏固線坑，
  並用螺絲固定 "根深柢固"
Supplement Information (Installation Gridline)