## Slide 1: Innovative Safety Initiative Award 2013
Innovation: “Trench Cooler”
Submit by: Wo Hing Construction Co. Ltd.
Contract title: 1/WSD/11(K) – Term Contract for Waterworks District K - Kowloon
Wo Hing Construction Co. Ltd. Contract No.：1/WSD/11(K)

## Slide 2
In Hong Kong, the temperature usually rise to 32℃ to 34℃ during summer. The hot weather had caused many heat stroke accidents in the past and some of them even resulting to fatal consequence. For construction industry, outdoor workers have to wear safety gears such as safety helmet and reflective jacket, which had induced overheat to the body of workers. Therefore, the invention of “Trench Cooler”can effectively ensure the health of workers against heat stroke by providing a cool environment for trench work.
33℃開工曝曬 地盤工中暑亡
烈日巡地盤 管工中暑亡
Wo Hing Construction Co. Ltd. Contract No.：1/WSD/11(K)

## Slide 3
Making of “Trench Cooler”
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)

## Slide 4
The idea of innovation was inspired by the air conditioning system of motor bus.
Wo Hing Construction Co. Ltd. Contract No.：1/WSD/11(K)

## Slide 5
Open 6 holes on a 2 metres long, 0.3 metre width soft hose. Install plastic bottle caps to each hole and seal them to avoid leakage of air.
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)

## Slide 6
Connect an air blower to one end of the soft hose and seal the other end of the soft hose.
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)

## Slide 7
Seal the connection of the blower and the soft hose with tape.
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)

## Slide 8
Turn on the blower to fill cool air inside the soft hose.
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)

## Slide 9
Open the bottle caps on the soft hose to let cool air jetting out to form a cool working environment.
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)

## Slide 10
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)
Test Results of
“Trench Cooler”
To ensure the workability, efficiency and reliability of “Trench Cooler”, 24 workers were being interviewed after testing of the invention, the results were satisfactory.

## Slide 11
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)
Advantages of
“Trench Cooler”

## Slide 12
Utilized used soft hose and plastic bottles which is environmental protection friendly;
The production process is simple and laboring free;
No complex installation and easy to use;
Easy to carry, soft hose can be folded;
Normal air blower dispersed sand and dust to contaminate surrounding environment. The air outlets of “Trench Cooler” concentrated the air flow that make it works more cleanly and efficiently.
The “Trench Cooler” can be placed at the top or at the bottom of the trench that it would not disturb the processing of the trench work, and it also provides a cool working environment in hot weather.
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)

## Slide 13
Wo Hing Construction Co. Ltd. Contract No. : 1/WSD/11(K)
Thank You