## Slide 1: Innovative Safety Initiative Award 2013 Jointly Organized by DEVB, CIC and HKCA
CHUN WO-CRGL-MBEC JOINT VENTURE
Contract No. HY/2009/19
Central- Wan Chai Bypass – Tunnel (North Point Section) and Island Eastern Corridor Link

## Slide 2: Gantry Crane Ultrasonic Warning System for Mobilization
Gantry crane is selected for lifting and transporting of pre-cast bridge segment at storage yard, due to heavy lifting and transportation efficiency.
There are two blind points while segment is lifting and the gantry operator is not able to notify.

## Slide 3
SWL 160 TON
Bang!

## Slide 4: Gantry Crane Ultrasonic Warning System for Mobilization
In order to eliminate the hazard, the pro-active warning system for gantry crane mobilizing on rail is installed by using the ultrasonic sensor to detect obstacle / pass-by worker on rail. The progressive visual is generated by flash light and audio warning sign is triggered by buzzer to crane operator.
The system also eliminates the blind point while segment is lifting, where the visual paths of gantry crane are blocked by segment. It is greatly appreciated by gantry operator.

## Slide 5: Gantry Crane Ultrasonic Warning System for Mobilization
General view of gantry crane

## Slide 6
Ultrasonic sensor
Gantry Crane Ultrasonic Warning System for Mobilization
Ultrasonic sensor
Control box

## Slide 7
Configuration and wire connection of control box
Gantry Crane Ultrasonic Warning System for Mobilization
Device set up on crane
Control box
Ultrasonic sensor

## Slide 8
Visual warning display & audio warning device installed at operating cabin
Gantry Crane Ultrasonic Warning System for Mobilization
Buzzer
Visual display

## Slide 9
Left side warning device detects worker walks near the leg of crane. Pre-warning visual and audio signal is given.
Worker walks near the leg of crane
Gantry Crane Ultrasonic Warning System for Mobilization

## Slide 10
Worker works close to the leg of crane
Gantry Crane Ultrasonic Warning System for Mobilization
Left side warning device detects worker walks closed to leg of crane, visual and audio warning signal is given.

## Slide 11
Left side warning device detects worker walks very closed to the leg of crane, stop operation in visual and audio warning is given.
Gantry Crane Ultrasonic Warning System for Mobilization
Worker walks very close to the leg of crane

## Slide 12
Ultrasonic sensor installed at leg of gantry crane
Gantry Crane Ultrasonic Warning System for Mobilization
Warning zone of ultrasonic warning device
Ultrasonic sensor

## Slide 13
1.5M
1M
0.5M
SWL 160 TON
Bi-Bi-Bi
Bi

## Slide 14
Warning zone | Range of warning zone | LED Light (Visual) | Warning sound (Audio) | Action should be taken by crane operator
Pre-warning zone | >1.2m | Point mark only | Bi (one tone) | Alert
Buffer zone | About 1.0 ~ 1.2m | Blue mark | Bi-Bi tone (3/4 sec.) | Alert
Buffer zone | About 0.8 ~ 0.9m | Green mark | Bi-Bi tone (1/2 sec.) | Prepare to slow down
Buffer zone | About 0.4 ~ 0.7m | Yellow mark | Bi-Bi-Bi (1/3 sec.) | Slow down
Stop zone | About 0.1 ~.03m | Red mark | Bi-Bi-Bi (1/5 sec.) | Stop at once
Gantry Crane Ultrasonic Warning System for Mobilization
Visual and Audio signal for warning zone and action taken